## Slide 1: Light-Emitting Diodes (LEDs)
An Overview of LED Technology
Generated by Aura AI

## Slide 2: What is an LED?
Semiconductor device that emits light when forward-biased
Invented 1962 (Nick Holonyak)
Works via electroluminescence

## Slide 3: How LEDs Work
P-type & N-type layers form a PN junction
Electrons recombine with holes -> photons released
Wavelength (color) -> band-gap energy

## Slide 4: Key Characteristics
Efficiency: 20-200 lm/W (vs. incandescent ~15 lm/W)
Longevity: 25,000-100,000 h
Fast switching: ns-range
Small size & robust

## Slide 5: LED Colors & Materials
Red - AlGaAs
Green - InGaN
Blue - InGaN (high band-gap)
White - Blue LED + phosphor or RGB mixing

## Slide 6: Advantages Over Traditional Light Sources
Lower power consumption
No warm-up time
Shock-resistant
Directional light -> less optics needed

## Slide 7: Common Applications
Lighting: home, street, automotive, horticulture
Displays: TVs, monitors, billboards, AR/VR
Indicators: appliances, wearables, IoT devices
Communications: Li-Fi, fiber-optic links

## Slide 8: LED Packaging & Types
Through-hole (T-1 3/4, 5 mm) - classic indicator
Surface-mount (SMD, 0805, 1206) - PCB integration
Chip-on-Board (COB) - high-density arrays
Flexible / OLED - bendable lighting

## Slide 9: Design Considerations
Forward voltage (Vf): 1.8 V (red) -> 3.6 V (blue)
Current limiting: resistors or constant-current drivers
Thermal management: heat-sinks, copper pours
Color Rendering Index (CRI) importance for indoor lighting

## Slide 10: Future Trends
Micro-LED displays - high brightness, low power
Smart/Connected LEDs - IoT integration, tunable color
Improved phosphors - higher CRI, lower blue-hazard
Sustainable manufacturing - recycling, eco-friendly materials

## Slide 11: Summary
LEDs are energy-efficient, long-lasting light sources
Wide range of colors & form factors
Continuously evolving for smarter, greener lighting solutions

## Slide 12: References
LEDs: Fundamentals, Materials, and Devices - B. O'Regan
IEEE Spectrum - "The LED Revolution" (2023)
https://www.ieee.org/led-resources
Manufacturer datasheets (Cree, Osram, Nichia)